## Slide 1: PPSv2018 introduction and scientific updates.
Nina Håkansson, Sara Hörnquist, Anke Thoss, Ronald Scheirer, Adam Dybbroe, Karl-Göran Karlsson

## Slide 2: Content
About the software
Introduction to the products
Scientific news in v2018
I use PPS
I do not use PPS yet

## Slide 3: PPS v2018
Software for cloud and precipitation products
Developed by NWCSAF
Polar orbiting satellites
Instruments (v2018)
  AVHRR
  VIIRS
  MODIS
I have used PPS v2014

## Slide 4: Products
Cloud mask
Cloud Probability (new)
Cloud Type
CTTH
  Cloud Top Temperature, Pressure and Height
Precipitating clouds
Cloud Physical Properties

## Slide 5: Cloud Mask (CMA)
Cloud mask
  Binary cloud mask
Extended product:
  Cloud filled
  Cloud contaminated
  Cloud free snow/ice
  Cloud free
Uses Thresholding:
  If features are not within what is reasonable for clear conditions it is a cloud. (simplified)
I will be using the cloud mask

## Slide 6: Cloud Mask (CMA)
Separate quality png
  Indicating pixels with low quality
In product (nc) file quality information is in flag cma_quality flag
Allows users to filter data.

## Slide 7: CMA News v2018
Thresholds updated to RTTOV12
Harmonized:
  Test order
  Cloudfilled / cloud contaminated
Increased POD cloudy
Slightly increased FAR
Slightly better Hitrate
Similar Kuipers Skill Score
V2018
RGB

## Slide 8: Cloud probabilities
Developed by CMSAF
Gives probability of cloud for each pixel.
Can be used as input to CTTH and CPP
Minimum cloudy probability limit is configurable.
SM_CMAPROB_CLOUD_THRESHOLD

## Slide 9
CMaprob in PPS 2018: Probabilistic cloud masks - Motivation
Goal:
  Complement CMA with a cloud mask expressed as cloud probabilities
Reason:
  Provide uncertainty in cloud masking
  Flexible use of the cloud mask
Examples of applications:
  Clear-conservative (SST/LST retrievals),
  climate-optimised (CM SAF Climate Data Records)
  cloud-conservative (cloud property retrievals)
Original CMaprob slides from: Karl-Göran Karlsson

## Slide 10
Cmaprob method
Simplified Bayesian theory (Naïve Bayesian)
The equation gives the probability that it is cloudy given an image feature vector F. The result is calculated as a product of the probabilities given by individual image features.
Individual feature probabilities are calculated from 10 years of collocated global AVHRR and CALIPSO-CALIOP observations

## Slide 11
Special features of the CMaprob method
Cloud probabilities can never be the same over surfaces with very different characteristics (e.g. bright vs dark, cold vs warm, day vs night, etc.)  Probabilities are calculated differently for several surface categories and for day and night!
To account for viewing angle dependencies and atmospheric conditions, several image features are constructed as differences from PPS pre-calculated thresholds (already accounting for these dependencies)

## Slide 12
RGB
(0.6, 0.9, 11 µm)
Clear water training
Snow cover land training
Merged final product
Demonstration of the use of different training statistics (from filtered CALIOP cloud masks) over different surfaces

## Slide 13
The meaning of resulting probabilities
The default version of CMaprob is tuned so that a 50 % threshold gives a globally optimized cloud mask.
Which clouds are detected varies with surface. Very thin cirrus is not possible to detect over very cold or very bright surfaces.
Best conditions are found over High Latitude Ocean surfaces where clouds with optical thicknesses down to 0.05 can be detected at the 50 % probability level

## Slide 14: Cloud probabilities validation
15 orbits NPP-data is used.
 | POD cloudy | POD clear
CMA | 88 | 83
CMAPROB-10 | 91 | 73
CMAPROB-50 | 82 | 89
CMAPROB-90 | 80 | 91

## Slide 15: Cloud Top Temperatur and Height
Temperature
Height
Pressure
Input one of:
  CMA
  Cloud Probability
Uses NWP-data
Height

## Slide 16: CTTH major development in last releases
RGB
v2012
v2014
v2018

## Slide 17: CTTH news in v2018
Algorithm replaced with neural network trained approach.
Significantly improved results!
Mean absolute error is reduced ~40%.
I note results look good also compared to MODIS-C6

## Slide 18: CTTH news in v2018
High clouds is placed higher.
Height of cloud edges/subpixel cloudiness improved
V2018
V2014

## Slide 19: NPP example 1
v2018
v2014
RGB
In the upper right corner I see that low and high clouds are better separated in version 2018.

## Slide 20: Example NPP 2
v2018
v2014
RGB
In version 2018 low clouds are placed lower.
In version 2018 the larger segment size for semi-transparent clouds is no longer needed.
  Less large squares with same height.

## Slide 21: CTTH method documented in article
  http://www.atmos-meas-tech.net/11/3177/2018/amt-11-3177-2018.html
I will check this out

## Slide 22: Cloud Type (CT)
Gives cloud type in 14 classes
I will be using the CT product

## Slide 23: CT news in v2018
Uses CTTH as input
Very Low clouds defined as:
  Clouds within 500m from ground
Better separates fractional from cirrus.
I notice large areas with fractional clouds (purple) in v2018 that was classed cirrus (blue) in v2014.
V2018
V2014

## Slide 24: Precipitating clouds
Only technical updates from v2014 and forward
In version 2018 nodata if no AMSU-data.
  Largest difference between the two versions.
Some differences due to updates in CT (CTTH as input)
V2018
V2014

## Slide 25: Cloud microphysical properties (CPP)
Developed by KNMI
Validated products:
  Cloud Phase
  Liquid water path
Extra products:
  Effective Radius
  Ice water path
  Cloud water path
  Cloud optical thickness
  Cloud water Paths

## Slide 26: CPP news v2018
Also benefits from improved CTTH
  If configured to use CTTH as input!
Most changes visible is due to changed CMA.
V2018
V2014

## Slide 27: CPP news v2018
Changed to use 3.7 instead of 1.6 when both are available.
Patch 2:
  10-30% faster processing of CPP
  (Not for GAC)
V2018
V2014
I look forward to faster CPP!
LWP
LWP

## Slide 28: Real time product demonstration
  http://nwcsaf.smhi.se/pps_v2018_product_demonstration.php
I will check this out

## Slide 29: Thanks for listening!
I need a break!