## Slide 1: PPS v2018 installation and running
2019-05-15
Sara Hörnquist
Nina Håkansson
Adam Dybbroe

## Slide 2: Did you listen to previous presentation today on PPS v2018 scientific aspects?
Yes
No

## Slide 3: Overview
Installation
  Using binaries
  From source code
Running PPS for one scene
  Different types of scripts
  Different parameters
Configuration
  How to configure
  What to configure (examples)
Installing patches
Running in operations with Pytroll (very shortly)

## Slide 4: What are your experiences about installation?
I have installed PPS using source code
I have installed PPS using binaries
I have tried installing PPS, but failed
I have never installed PPS

## Slide 5: What are your plans for installation?
I will install PPS using source code
I will install PPS using binaries
I do not know yet

## Slide 6: Why installing from binaries?
Simplest way of installation, just a few commands
All third party software are either included or automatically fetched via pip
All PPS code included
Binaries available for:
  CentOS/RHEL 7.5
  Ubuntu 16.04
You use a Linux distribution where no binary is available
You can use already existing third party s.w.
You can make more settings your way
Root access is not necessary
All patches are available as source code
Why installing from source code?

## Slide 7: Binaries available
These are currently available:
CentOS/RHEL 7.5
Ubuntu 16.04
Other needs:
Other (newer) versions can be considered if requested
openSUSE can be considered if requested

## Slide 8: Under which OS do you intend to install and run PPS v2018?
CentOS 6 | 
CentOS 7 | 
RHEL 6 | 
RHEL 7 | 
Ubuntu 14 | 
Ubuntu 16 | 
Ubuntu 18 | 
openSUSE | 
SUSE SLES | 
Fedora | 
other RPM based | 
other Debian based | 
Other Linux | 
Non Linux | 
Don’t know | 

## Slide 9: Prepare for installation of binaries
Make sure the user is allowed to install in intended directories:
CentOS/RHEL
In the file /etc/sudoers this line must be available:
sara ALL=/usr/bin/yum
Ubuntu
In the file /etc/sudoers this line must be available:
sara ALL=/usr/bin/apt-get
Where ‘sara’ is an example of a user name.

## Slide 10: Installing from binaries
Instruction found on helpdesk: “PPSbinaryinstallation_v2018.pdf”
The steps are:
Create directories needed
Download packages from helpdesk
Unpack tar-files
Run installation script
Copy PPS data, to final destination
Unpack CPP-ancillary data and reference data
Done!

## Slide 11: Installing from binaries (CentOS/RHEL)
cd ppswork
tar xvfz pps_centos75_scripts.tgz
cd ../RPMS
tar xvfz pps_v2018_centos_rpms.tgz
../ppswork/centos75_yum_install_pps.sh
cd ../data
rsync –a /usr/shape/pps/ .
Prepare:
Download PPS binary packages from helpdesk
Create directories needed (ppswork, RPMS, data)

## Slide 12: Installing from binaries (Ubuntu)
cd ppswork
tar xvfz pps_ubuntu_scripts.tgz
cd ../debian
tar xvfz pps_v2018_ubuntu16.tgz
../ppswork/ubuntu16_dpkg_install_pps.sh
cd ../data
rsync –a /usr/shape/pps/ .
Prepare:
Download PPS binary packages from helpdesk
Create directories needed (ppswork, debian, data)

## Slide 13: Destinations for the binary installation
This is not configurable
AAPP, AHAMAP, ACPG&CPP installs under /opt
Other packages installs under /usr
PPS data installs under /usr/share/pps, but is suggested to copy to, and use in eg.: $HOME/data

## Slide 14: Installing from source code, Third Party sw 1(2) without Conda
Start with third party s.w.
The needs are listed on the helpdesk
Existing installations can be used
  PPS accepts most versions and combinations –though we can not guarantee that all versions and combinations works. (See also comments in helpdesk.)
Both python 2 (≥ 2.7) and python 3 (≥ 3.3) works, with matching python packages.
Install remaining packages
  Python packages: use pip or easy_install
  Not python packages: individual installation procedure
  All packages can be found on helpdesk, if preferred

## Slide 15: Installing from source code, Third Party sw 2(2) with Conda
An easier way to install all third party s.w.
  Have a Conda environment (must be python3)
  Install all third party s.w. with: ppsv2018_1_conda_environment.yml (provided on helpdesk)
  Some special measures for further PPS installation, see installation note
  Install pps_nwp with pip
  Only works for PPS v2018.1 and later

## Slide 16: Installing from source code
Make sure your PYTHONPATH includes:
  Where third party s.w. python packages are installed (if not using the standard place)
  Where you plan to install pps_nwp (unnecessary if using pip)
Instructions in Installation_Notes_v2018.pdf
Download PPS packages from helpdesk
Install the packages in the following order
  pps_nwp
  AHAMAP
  ACPG
  CPP
Optional: download and install test data; download reference data

## Slide 17: Install pps_nwp
tar xvfz pps_nwp-1.0.1.tar.gz
cd pps_nwp
python setup.py install --prefix=/local_disk/opt
tar xvfz pps_nwp-1.0.1.tar.gz
pip install <path_to_pps_nwp>/pps_nwp/
or using easy_install:
Using pip:

## Slide 18: Install AHAMAP
tar xvfz ahamap_v2018.tar.gz
cd ahamap_v2018
./configure - -prefix=/local disk/opt/AHAMAP/v2018 - -with-proj=/usr/include,/usr/lib64 - -with-python2
make
make check
make install

## Slide 19: Install ACPG
tar xvfz acpg_v2018.tar.gz
tar xvfz acpg_staticdata_v2018.tar.gz
cd acpg
./configure --prefix=/local disk/opt/ACPG/v2018 --with-ahamap=/local disk/opt/AHAMAP/v2018 --with-proj= /usr/include,/usr/lib64 --with-hdf5=/usr/include,/usr/lib64 --with-netcdf=/usr/include,/usr/lib64 --with-python2 --datadir =/local disk/data/pps --with-gac=no
make
make check
make install
make install-data

## Slide 20: Install ACPG
tar xvfz acpg_testdata_v2018.tar.gz
cd acpg
make install-testdata
ACPG testdata is optional
Install it after ACPG has been installed

## Slide 21: Install CPP
tar xvfz cpp_v2018.tar.gz
cd cpp_v2018
./configure - -prefix=/local disk/opt/ACPG/v2018 - -with-proj=/usr/include,/usr/lib64 - -with-python2
make
make check
make install
cd /local_disk/data/import/CPP_data/source
tar xvfz cpp_ancdata_v2014.tgz
CPP is optional
CPP should be installed in the same directory as ACPG

## Slide 22: Which PPS products are you interested in?
Cloud Mask
Cloud Probability
Cloud Type
Cloud Physical Properties
Precipitating Clouds
Cloud Top Temperature, Height and Pressure

## Slide 23: Preparations for processing
Download and install
Make sure you have a data supply (or test data as a start)
  At least: satellite data and NWP-data
  Optional: OSISAF sea ice data
Activate soure_me or .profile_pps
  Which one depends on your environment

## Slide 24: Running PPS for one scen with one main scripts
There are a few main scripts:
ppsRunAll.py
  Run all products serial (can be parallel with-in a product)
ppsRunAllParallel.py
  Run products in parallel, when possible
ppsRunAllParallel_inclCMaProb.py
  (where Cloud Probability can not be input to CTTH or CPP)
Special scripts for GAC-processing.
python ppsRunAll.py --hrptfile metop01_20151026_0132_ 16101/hrpt_metop01_20151026_0132_16101.l1b

## Slide 25: Running PPS for one scene, with one script per product 1(2) Prepare Steps
python ppsMakeAvhrr.py --hrptfile metop01_20151026_0132_ 16101/hrpt_metop01_20151026_0132_16101.l1b
python ppsMakePhysiography.py --hrptfile metop01_20151026_0132_16101/hrpt_metop01_20151026_0132_16101.l1b
python ppsMakeNwp.py --hrptfile metop01_20151026_0132_16101/hrpt_metop01_20151026_0132_16101.l1b
python ppsCmaskPrepare.py --hrptfile metop01_20151026_0132_16101/hrpt_metop01_20151026_0132_16101.l1b
python ppsPrecipPrepare.py --hrptfile metop01_20151026_0132_16101/hrpt_metop01_20151026_0132_16101.l1b

## Slide 26
python ppsCmask.py --hrptfile metop01_20151026_0132_ 16101/hrpt_metop01_20151026_0132_16101.l1b
python ppsCtth.py --hrptfile metop01_20151026_0132_ 16101/hrpt_metop01_20151026_0132_ 16101.l1b
python ppsCtype.py --hrptfile metop01_20151026_0132_
16101/hrpt_metop01_20151026_0132_16101.l1b
python ppsCpp.py --hrptfile metop01_20151026_0132_
16101/hrpt_metop01_20151026_0132_16101.l1b
python ppsPrecip.py --hrptfile metop01_20151026_0132_
16101/hrpt_metop01_20151026_0132_16101.l1b
python ppsCmaskProb.py --hrptfile metop01_20151026_0132_ 16101/hrpt_metop01_20151026_0132_16101.l1b
Running PPS for one scene, with one script per product 2(2) Products

## Slide 27: Run a selection of PPS products
Please mind the dependencies! (see image on next slide)
Example: only CMa and CTTH
One script, use parameters:
python ppsRunAll.py --hrptfile metop01_20151026_0132_16101/hrpt_ metop01_20151026_0132_16101.l1b --no_ctype --no_cpp --no_precip
Products scripts, chose your scripts:
Preparation steps…
python ppsCmask.py --hrptfile …
python ppsCtth.py --hrptfile ..
python ppsCtype.py –hrptfile ..
python ppsCpp.py –hrptfile ..
python ppsPrecip.py --hrptfile ..
python ppsCmaskProb.py –hrptfile …

## Slide 28: PPS Product Dependencies (simplified)
CMa
CTTH
Ctype
Precip
CPP
CMa-prob
Pre-proc.

## Slide 29: What instruments are you interested in?
AVHRR
VIIRS
MODIS
AMSU/MHS (only Precip product)
MERSI-2 (not yet available in PPS)

## Slide 30: Different ways to call the PPS scripts
It is the same call for all scripts. ppsCmask.py as example
python ppsCmask.py --hrptfile metop01_20151026_0132_ 16101/hrpt_metop01_20151026_0132_16101.l1b
python ppsCmask.py --pfsfile AVHR_xxx_1B_M03_ 20160202024003Z_20160202024303Z_N_O_20160202031844Z
python ppsCmask.py --csppfile npp_20170502_1454_28563/ GMTCO_npp_d20170502_t1457346_e1458570_b28563_c20170502150352002546_cspp_dev.h5
python ppsCmask.py --modisfile MYD021KM.A2014272. 0215.006.2014274142955.hdf
python ppsCmask.py --platform_orbit metop01 16101
python ppsCmask.py --anglesfile S_NWC_sunsatangles_ metopb_16101_20151026T0132000Z_20151026T0132598Z.nc
The last two work for both AVHRR, MODIS and VIIRS.
Short commands: -hf, -pf -cf, -mf, -po, -af

## Slide 31: Running PPS for VIIRS data high or low resolution
High resolution, one granule:
python ppsMakeViirs.py --csppfile npp_20170502_1454_28563/ GITCO_npp_d20170502_t1457346_e1458570_b28563_c20170502150352002546_cspp_dev.h5
Low resolution, one granule:
python ppsMakeViirs.py --csppfile npp_20170502_1454_28563/ GMTCO_npp_d20170502_t1457346_e1458570_b28563_c20170502150352002546_cspp_dev.h5
Low resolution, all granules in directory: npp_20170502_1454_28563
python ppsMakeViirs.py --platform_orbit npp 28563

## Slide 32: How to configure, after source code installation
NB! If configure is correctly run, none or few changes are necessary.
source_me or .profile_pps
  Created at installation
  In <acpg-source-code>
  Must activate before processing
pps_config_common.cfg
  in <acpg-installation>/cfg
pps_basic_configure.py
  In <acpg-installation>/cfg
pps_nwp.ini
  Find template in pps_nwp/cfg
  In you want to change it: Place in <acpg-installation>/cfg

## Slide 33: How to configure, after installation with binaries 1 (2)
NB! Normally only a few changes in source_me/.profile_pps are necessary.
source_me or .profile_pps
  Find in <acpg-installation>/cfg
  Copy to where you run the code.
  Modify if wanted. (at least DATA_DIR)
  Must activate before processing
pps_config_common.cfg
  Find in <acpg-installation>/cfg
  If you want to change it: copy to any location; set SM_CFG_FILE in source_me/.profile_pps

## Slide 34: How to configure, after installation with binaries 2 (2)
pps_basic_configure.py
  Find in <acpg-installation>/cfg
  If you want to change it: Copy to a location in your PYTHONPATH. This location must, in PYTHONPATH, come before <acpg-installation>/cfg.
pps_nwp.ini
  Find template in pps_nwp/cfg
  If you want to change it: copy to any location; set PPS_NWP_CONFIG_FILE in source_me/.profile_pps

## Slide 35: Configurations in source_me/.profile_pps, examples
Path to 3rd party s.w.
  Normally set while running ./configure or installing binary.
  AAPP_PREFIX must be set, if processing global Metop.
  H4TOH5_EXEC must be set, if processing MODIS.
Paths to where to have data (input/intermediate/output), possible to tailor.
SM_DONT_COMBINE_LATLON_AND_NXNY –in case of problems
SM_LATLON_IN_NETCDF_<pge>
SM_CPP_USE_CMAPROB for CMa-prob as input to CPP
PPS_HOOK_CONFIGFILE, if you want hooks (eg. for pytroll-pps-runner)

## Slide 36: Configurations in pps_config_common.cfg, examples
Which datasets to have in output files.
  Example for Cloud Mask: with or without
  Cloud Mask (including binary cloudmask)
  Aerosol Flag
  Dust Flag
  Processing Flags
  Test Flags (mainly for development)
  Mind dependencies!
(ctth)USE_CMAPROB for CMa-prob as input to CTTH
A few more about input.

## Slide 37: Configurations in pps_basic_configure.py, example
Many variables are read from source_me/.profile_pps –better to change them there than in pps_basic_configure.py.
You might want to change:
IMAGES Which products and satellite to make png-images for. (No images if: IMAGES={} )
NWP_MAXIMUM_TIME_DEVIATION + more for NWP
NWP_EXTRA_PARAM (for user convenience)
CPP_GENERATE_PROCESSING_FLAG, CPP_GENERATE_ERROR_ESTIMATES Set the wanted output for CPP.
etc.

## Slide 38: Configurations in pps_nwp.ini, examples
For most uses, this file is not necessary.
hydbrid_level_selection:
  Must be set if NWP-file use a subset of levels, eg. 91 levels of originally 137. Set it to match your selection.
  Can be set to speed up processing. Recommended setting: hybrid_level_selection = [x for x in range(49,138,2)]
Preferred NWP-fields for a certain NWP-feature. (Usually not necessary, pps_nwp is flexible.)

## Slide 39: I am interested in configuring PPS my own style:
Yes
No
Maybe

## Slide 40: Are my configurations okey?
If you do not intend to run all PGE:s:
If you have made substantial changes in pps_config_common.cfg:
Test your configuration with: ppsCheckPgeConfig.py
Example:
python ppsCheckPgeConfig.py CMA CTTH CT
CMa
CTTH
Ctype
Precip
CPP
CMa-prob
Product dependencies
(simplified)

## Slide 41: Installing Patches, source code
We deliver both:
  A patch, only for changed packages, to be applied on top of latest version.
  NB! Patch must be applied on latest version, not second- last, or else.
  A full delivery, with all current packages including patch.
Static data and test data are seldom replaced; if you do not want to download them again… (Though replaced in v2018.2!)

## Slide 42: Installing Patches, binaries
The packages (per s.w.) are never patched, just replaced.
One or several packages might be replaced in a patch-release.
We deliver both:
  Tar-ball ’patch’: only the replaced packages
  Tar-ball ’including patch’: all the current packages
  NB! Patch-only must be applied on latest version, not second-last, or else.
  First un-install old installation (with provided script)
  Then install the new one (with provided script)

## Slide 43: More information:
For more info about installation, see:
  Installation notes
  Binary installation notes
  User Manual, installation part
For more info about running, see:
  User Manual, operations part
For more info about configurations see:
  User Manuals, both parts
  The configuration files them selves
  Release notes, for news about configuration

## Slide 44: Running PPS operationally with Pytroll
A brief introduction
You can use a scheduler of your own if you prefer, but Pytroll is a good option.
This part with help from:
Adam Dybbroe

## Slide 45: Running PPS with Pytroll
Pytroll runner on Github:
  https://github.com/pytroll/pytroll-pps-runner.git
Using Posttroll for messaging

## Slide 46: Pytroll-pps-runner
Listens to messages from the level-1 runners
Using threads
Make call to the PPS scripts
  ppsRunAll.py
  ppsCmaskProb.py
Send messages in the end using PPS post hook

## Slide 47: Running PPS with Pytroll
PPS runs on VIIRS segments as they are finished
Collecting the PPS granules in the end (when enough data on your area of interest has been processed)
  Using Pytroll-collectors

## Slide 48: Running PPS with Pytroll
Making cloud product imagery (png, GeoTIFF, netCDF) output on areas of interest
  Using Satpy (and Pyresample, etc)

## Slide 49: Running PPS with Pytroll
Flow - VIIRS:
Get level-1 data: move_it_client_sdr
Run PPS: pps2018_runner
Collect/gather all PPS results on several segments into one set covering the area of interest: pps_viirs_gatherer

## Slide 50: Running PPS with Pytroll
Flow - VIIRS:
Get level-1 data: move_it_client_sdr
Run PPS: pps2018_runner
Collect/gather all PPS results on several segments into one set covering the area of interest: pps_viirs_gatherer
Remap and make imagery: pps_imagery

## Slide 51: Running PPS with Pytroll
Don’t hesitate to get in contact with the Pytroll community:
  Pytroll.org
  Pytroll-slack (get automatic invitation via home page)

## Slide 52: Are you interested in another online session about running PPS with Pytroll?
Yes
No

## Slide 53: Any questions?
Sara.Hornquist@smhi.se